MODEL WATERSHED

RULES AND REGULATIONS

AUGUST 3, 1995 FINAL DRAFT

Pursuant to the authority vested in the State Commissioner of Health, by Section 1100 of the Public Health Law, Section 150.1  of Part 150, Title 10 (Health) of the Official Compilation of Codes, Rules and Regulations of the State of New York, to be effective upon filing in the Office of the Department of State is hereby amended to read as follows:

# SECTION 150.1, CITY OF ITHACA, TOMPKINS COUNTY:

A.	Applicability:  The rules and regulations set forth in this Section, duly made and enacted in accordance with the provisions of Sections 1100- 1107 of the Public Health Law shall apply to the source of water supply of City of Ithaca, Tompkins County.  Said source of water supply shall include all reservoirs of the public water supply of the City of Ithaca on Six Mile Creek and the drainage area tributary to said reservoirs and the streams entering them. Would need to engage Caroline, Danby and Dryden in this discussion.  I don’t think we can leave it this vague and broad sweeping.

B.	Statement of Purpose:  Sources of water supplies are inherently exposed to the introduction of pollutants that may adversely affect their water quality.  The introduction of pollutants that typically cause adverse effects on water quality include, but are not limited to:

1.	Untreated regular discharges to either surface or ground water;

2.	Accidental or intentional introductions caused by poor management practices in any residential, agricultural, commercial, industrial, or other activity;

3.	Naturally occurring water, land, and air resource contributions.

Sources of water supplies may be subject to contamination due to either the improper management or inappropriate placement in relation to a source of water supply of a system, facility, and or activity.  The people of the State of New York have a right to expect, and the Commissioner of Health is obligated to see, that feasible precaution and measure is taken to protect a source of water supply from contamination, and that safe drinking water is available from all public water systems.

In order to assure the adequate protection of the source of water supply of the City of Ithaca, the following rules and regulations have been promulgated.

C.	Definitions:

1.	Aquifer shall mean the water-saturated subsurface geologic formations that are now or may subsequently be developed for use by a public water system.

2.	Aquifer recharge area shall mean the land area where precipitation, snow and rain percolates directly through the ground to an aquifer and shall be delineated by the Commissioner of Health.  The aquifer recharge area shall also be known as Zone II-G.

I believe there is a missing component here in that groundwater provides all of a stream’s base (low) flow.  Meaning that contaminated aquifers are our problem as well.

3.	Barnyard shall mean that area used for the storage of domestic animals where existing or planned farm activities will result in a concentration of animal waste that if not managed properly, has the potential of contaminating the water supply source of the City of Ithaca.

4.	Best management practices (BMP) shall mean the methods, measures or practices determined to be the most practical and effective in preventing or reducing the impact of pollutants generated by nonpoint sources to a level compatible with water quality standards established pursuant to section 17-0301 of the ECL.  BMP include, but are not limited to, structural and nonstructural controls and operations and maintenance procedures.  BMP can be applied before, during or after pollution producing activities to reduce or eliminate the introduction of pollutants into receiving waters.

a.		Standard BMP for agricultural activities shall include the latest version of the following:

i.)	The publication “Controlling Agriculture Nonpoint Source Water Pollution in New York State - A Guide to the Selection of Best Management Practices to Improve and Protect Water Quality” (1991), published by the Bureau of Technical Services and Research, Division of Water, NYSDEC, 50 Wolf Road, Albany, NY 12223; or,

ii.)	The publication “Agricultural Management Practices Catalogue for Nonpoint Source Pollution Prevention and Water Quality Protection in New York State” (1992), published by the Bureau of Water Quality Management, Division of Water, NYSDEC, 50 Wolf Road, Albany, NY 12223; or,I can contact Craig Schutt, TC SWCD to find out.

ii.)	The property, facility and/or activity’s Whole Farm Planning Program.

b.	Standard BMP for non-agricultural land disturbing activities shall include the latest version of the following:

i.)	The publication "Reducing the Impacts of Stormwater Runoff for New Development" (1992) as amended from time to time, published by the Bureau of Water Quality Management Division of Water, NYSDEC, 50 Wolf Road, Albany, NY 12223; or,

ii.)	The publication “New York Guidelines for Urban Erosion and Sediment Control" (1991) as amended from time to time, published by the Soil and Water Conservation Society, 100 S. Clinton Street, Room 771, Syracuse, NY, 13261: or,

iii.)	The publication “Construction Management Practice Catalogue for Nonpoint Source Pollution Prevention and Water Quality Protection in New York State" (1992) as amended from time to time, published by the Bureau of Water Quality Management, Division of Water, NYSDEC, 50 Wolf Road, Albany, NY 12223: or,

iv.)	The publication “Silviculture Management Practice Catalogue for Nonpoint Source Pollution Prevention and Water Quality Protection in New York State" (1993) as amended from time to time, published by the Bureau of Water Quality Management, Division of Water, NYSDEC, 50 Wolf Road, Albany, NY 12223.

5.	Contamination shall mean any substance or characteristic which will make water unsuitable or unsafe including a constituent or characteristic in an amount that exceeds allowable limits established by the Commissioner of Health.

6.	Chloride salt shall mean the solid compounds or the solutions of potassium chloride (commonly used as fertilizer), calcium chloride (commonly used for winter road maintenance) or sodium chloride (commonly used for winter road maintenance and water softener regeneration).

7.	Community water system shall mean a public water system that serves at least five service connections used by year-round residents or regularly serves at least 25 year-round residents.

8.	Discharge shall mean the disposal, injection, emission, application, dumping, spilling, leaking, washing off, running off, draining or placing of any solid, semi-solid, liquid, or any other non-gaseous waste or other substance into or onto any land or water so that such waste or other substance may directly or indirectly enter into any watercourse or groundwater.

9.	Disposal shall mean the abandonment , discharge, injection, spilling, leaking or placing of any substance so that such substance or any related constituent thereof may enter the environment.  Disposal also means the thermal destruction of waste or hazardous waste and the burning of such waste as fuel for purposes of recovering useable energy.

10.	Environmental impact assessment shall mean a written evaluation that provides a description of a proposed project or development and a detailed analysis of its potential environmental effects.

11.	Farm shall mean the land used in a single operation for the production for sale of, including but not limited to, crops, horticultural and aquacultural products, livestock and fowl or livestock and fowl products of an annual average (over the past two years) gross sales amount of $10,000 or more.

12.	Fertilizer shall mean any organic or inorganic substance of natural or synthetic origin that is added to the soil to supply elements intended to be a beneficial nutrient for plants.

13.	Flood plain (100-year) shall mean land indicated to be susceptible to being inundated by a flood with a probability of occurrence of no greater than one percent in any given year by the Federal Emergency Management Agency or its predecessor, the Department of Housing & Urban Development.  We need new flood plain maps – the LIDAR is done, but last I heard, the State ran out of money to produce new maps from the pix.

14.	Ground water shall mean water below the land surface in a saturated zone of soil or rock.  This includes perched water separated from the main body of ground water by an unsaturated zone.

15.	Ground water management area shall mean the portion of a  ground water watershed delineated by a protection zone.

16.	Hazardous substance shall mean a substance as defined in 6 NYCRR 597.1 (a)(3) and the Federal Clean Water Act Section 309, as each may be amended.

17.	Hazardous waste shall mean a waste as defined in 40 CFR 261.3 or 6 NYCRR 371.1 as each may be amended.  The starting point for generators in determining if a waste is hazardous is 40 CFR 261.11, criteria for listing hazardous waste:

a.)	First, determine if the waste is excluded from regulation as hazardous under 40 CFR 261.4

b.)	Second, check the hazardous wastes list in Subpart D of 40 CFR 261.

c.)	If the waste is not listed or excluded, determine if the waste exhibits one of the four hazardous waste characteristics (ignitability, corrosivity, reactivity, toxicity) described in Subpart C of 40 CFR 261

18.	Human excreta shall mean human feces and urine.

19.	Industrial waste shall mean any liquid, gaseous, solid or waste substance or combination thereof resulting from any process of industry, manufacturing, trade, or business or from the development or recovery of any natural resources, that may cause or might reasonably be expected to cause pollution of the waters of the state in contravention of the standards adopted by the state.

20.	Junkyard shall mean an area where {a specified number} of unregistered motor vehicles are being accumulated for purposes of disposal, resale of used parts, or reclaiming certain materials such as metal, glass, fabric and/or the like.

21.	Land management area shall mean the portion of land adjacent to a lake, reservoir, or watercourse delineated by a protection zone.

22.	Land application of sewage treatment effluent shall mean the distribution of municipal or industrial sewage treatment effluent by point discharge(s), spray irrigation, or direct flow, over the land surface with or without an under drain system.

23.	Linear distance shall mean the shortest horizontal distance from the nearest point of a structure or object to the high water level of a lake, reservoir or watercourse or to the edge, margin or steep bank forming the recorded high water level of a lake, reservoir or watercourse.

24.	Nonpoint source shall mean any source of water pollution or pollutants that is not a discrete conveyance or point source permitted pursuant to Title 7 or 8 of the ECL.

25.	Other wastes shall mean garbage, refuse, decayed wood, sawdust, shavings, bark, sand, lime, cinders, ashes, offal, oil, tar, dyestuffs, acids, chemicals, ballasts and all other disposed of matter, not sewage or industrial wastes, that may cause or might reasonably be expected to cause pollution of the waters of the state in contravention of standards adopted by the state.

26.	Pesticide shall mean any substance or mixture of substances intended for preventing, destroying, repelling, or mitigating any pest; and any substance or mixture of substances intended for use as a plant regulator, defoliant or desiccant.

27.	Petroleum shall mean oil or petroleum of any kind and in any form including but not limited to oil, petroleum, fuel oil, oil sludge, oil refuse, oil mixed with other waste, crude oil, gasoline and kerosene.

28.	Point source shall mean any discernible, confined and discrete conveyance, including but not limited to any pipe, ditch, channel, conduit, well, discrete fissure, container, rolling stock, concentrated animal feeding operation, vessel or other floating craft, or landfill leachate collection system from which pollutants are or may be discharged.  This term does not include agricultural storm water discharges and return flows from irrigated agriculture.

29.	Pollutant shall mean :dredge spoil; solid waste; incinerator residue; sewage; garbage; sewage sludge; munitions; chemical wastes; biological materials; radioactive materials; heat; wrecked or disposed of equipment; rock; sand and industrial, municipal and agricultural waste discharged into water; and ballast which may cause or might reasonably be expected to cause pollution of the waters of the state in contravention of the standards by the state.

30.	Protection zone shall mean that land and/or water surface area within a surface water and/or ground water management zone as delineated herein; they shall be designated Zone I-S, Zone II-S, Zone III-S, and Zone IV-S for surface water protection zones and Zone I-G, Zone II-G, and Zone III-G for ground water protection zones.

31.	Public water system shall mean a community, noncommunity, or nontransient noncommunity water system which provides piped water to the public for human consumption, if such system has at least five service connections or serves an average of at least 25 individuals daily at least 60 days out of the year.  Such term includes:

a.)	collection, treatment, storage and distribution facilities under control of the City of Ithaca and used with such system; and,

b.)	collection or pretreatment facilities not under such control which are used by such system.

33.	Radioactive material shall mean any material in any form that emits radiation spontaneously. Radiation shall mean ionizing radiation; that is, any alpha particle, beta particle, gamma ray, x-ray, neutron, high-speed proton, and any other atomic particle producing ionization, but shall not mean any sound or radio wave, or visible, infra-red or ultraviolet light.

34.	Recreational activities shall mean fishing, swimming, wading, use of recreational vehicles or any other similar activity.

35.	Refuse shall mean, in accordance with 6 NYCRR Part 360, anything putrefactive or nonputrefactive that is disposed of or rejected as useless or worthless.

36.	Refuse disposal area shall mean land used for the depositing of refuse except that it shall not include the land used for the depositing of refuse from a single family, a member of which is the owner, occupant or lessee of said land, or any part of a farm on which animal wastes  and other organic nutrients are deposited as fertilizer.  (This definition includes, but is not limited to, those areas commonly referred to as landfills and sanitary landfills.)

37.	Reservoir shall mean any natural or artificial lake or pond that is tributary to or serves as a source of the community water system.

38.	Section or this Section shall mean these watershed rules and regulations that can be found in Chapter III of Title 10 (Health) of the Official Compilation of Codes, Rules and Regulations of the State of New York.

39.	Septage shall mean, in accordance with 6 NYCRR Part 360, the contents of a septic tank, cesspool or other individual sewage treatment facility that receives domestic sewage wastes.

40.	Sewage shall mean the water carried human or animal wastes from residences, buildings, industrial establishments or other places, together with such ground water infiltration and surface water as may be present.  The admixture with sewage, industrial waste and/or other waste shall also be considered “sewage”.

41.	Sewage sludge shall mean the accumulated semisolids or solids resulting from treatment of waste from publicly owned or privately owned or operated sewage treatment plants. Sewage sludge does not include grit or screening, or ash generated during the incineration of sewage sludge.

42.	Sewage treatment facility shall mean any system used for treating sewage, including an onsite treatment system.

43.	Solid waste shall mean any garbage, refuse, sludge from a waste treatment plant, water supply treatment plant or air pollution control facility and other disposed of material, resulting from industrial, commercial, mining and agricultural, and from community activities, but does not include solid or dissolved materials in domestic sewage, or solid or dissolved materials in irrigation return flows or industrial discharges that are point sources subject to permit under 33 USC 1342, as amended (86 Stat.880), or source, special nuclear or by-product material as defined by the Atomic Energy Act of 1954 and as amended (68 Stat.923) except as may be provided by existing agreements between the State of New York and the government of the United States.

44.	Source of water supply shall mean any ground water, aquifer, surface water body or watercourse from which by any means water is regularly taken either periodically or continuously for drinking, culinary or food processing purposes or which has been classified for present or future public beneficial use as a source for domestic or municipal purposes.

45.	Stream shall mean a body of water moving over the earth’s surface in a channel or bed.  An intermittent stream shall mean a stream that during certain times of the year goes dry and periodically receives ground water inflow this addresses base flow but I don’t know that any protections are afforded via the connection.  A drainage ditch, swale or surface feature that contains water only during and immediately after a rainstorm, and never receives ground water inflow, shall not be considered to be an intermittent stream.

46.	Surface water management area shall mean the portion of a lake, reservoir or watercourse watershed delineated by a protection zone.

47.	Toxic substance shall mean, a substance that exhibits the characteristic of toxicity as described in 40 CFR 261.24. “Toxicity characteristic” is determined if an extract taken and analyzed in accordance with Appendix II of 40 CFR 261, from a representative sample of the substance, contains contaminants that exceed the concentrations listed in Table 1 of that Part.

48.	Treatment works shall mean, any plant, disposal field, lagoon, pumping station, constructed drainage ditch or surface-water intercepting ditch, incinerator, area devoted to sanitary landfills or other works not specifically mentioned herein, installed for the purpose of treating, neutralizing, stabilizing or disposing of sewage, industrial waste or other wastes.

49.	Waste shall mean any garbage, refuse, sludge from a waste treatment plant, water supply treatment plant, or air pollution control facility, and any other disposed of material, including solid , liquid, semisolid, or contains gaseous material resulting from industrial, commercial, mining and agricultural operations and from community activities, but does not include solid or dissolved material in domestic sewage, or solid or dissolved materials in irrigation return flows or industrial discharges which are point sources subject to permits under section four hundred two of the federal Water Pollution Control Act , as amended (86 Stat.880), or source, special nuclear or by-product material as defined in the Atomic Energy Act of 1954, as amended (68 Stat.923) except as may be provided by existing agreements between the state of New York and the government of the United States.

50.	Water supply shall mean the source of water supply for the City of Ithaca.

51.	Water supply intake shall mean the point at which the water supply enters the City of Ithaca.

52.	Watercourse shall mean a visible path through which surface water travels on a regular basis, including an intermittent stream, which is tributary to the Six Mile Creek.  A drainage ditch, swale or surface feature that contains water only during and immediately after a rainstorm shall not be considered to be a watercourse.

53.	Watershed shall mean all of the land and water surface area that contributes water to a specific lake, watercourse, ground water or surface or ground water supply.

54.	Well shall mean any present or future artificial excavation used as a source of public water supply that derives water from the interstices of the rocks or soils in which it penetrates, including bored wells, drilled wells and driven wells and excluding ditches or tunnels that lead ground water to the surface by gravity.

55.	Well-head protection area shall mean the area surrounding a well or spring or spring basin... {final definition will be determined by the public water system with assistance from the Commission of Health}.  This shall also be known as Zone I-G.

56.	Whole Farm Planning Program shall mean that program designated to implement best management practices on farms (farms as defined previously) in order to eliminate or minimize sources of nonpoint source pollution.

57.	Zone I-G shall mean the well-head protection area, including the cone of influence ... {final definition will be determined by the public water system with assistance from the Commissioner of Health}.

58.	Zone II-G shall mean the recharge area of aquifers on the upflow side of the withdrawal area (the land and water surface area that contributes water to Zone I-G, identified by an annular area bounded by Zone I-G and a distance from Zone I-G determined by the public water system with the assistance from the Commissioner of Health, that is expected to provide an adequate microbiological treatment barrier for water entering Zone I-G) ... {final definition will be determined by the public water system with assistance from the Commissioner of Health} .

59.	Zone III-G shall mean the watershed tributary to the recharge area of aquifers or the contributing land and water surface from which the aquifer is replenished by runoff through the recharge area of aquifers ... {final definition will be determined by the public water system with assistance from the Commissioner of Health} .

60.	Zone I-S shall mean a surface water protection zone and shall be the area within 1,000 feet linear distance of any lake or reservoir water supply intake, and within 1,000 feet linear distance upstream of a watercourse water supply intake.

61.	Zone II-S shall mean a surface water protection zone and shall be the area :

a.)	within one mile linear distance upstream of a water supply intake in a lake; or

b.)	the entire surface area and watercourse within one mile upstream of a reservoir intake; or

c.)	within one mile linear distance upstream of a water supply intake in any watercourse.

62.	 Zone III-S shall mean a land and water protection zone and shall be the area:

a.)	of the watershed, tributary to the water supply within five miles upstream of a lake intake; or

b.)	within the entire upstream watershed of reservoir intake; or

c.)	within the upstream tributary watershed of any water supply intake in any watercourse.

63.	Zone IV-S shall mean a land and water protection zone incorporating any or all of the remainder of an intake's upstream watershed not covered in Zone III-S.

E.	General Provisions:

1.	Protection zones shall be delineated for each source of water supply for both ground and surface water by the Commissioner of Health in conjunction with the public water system for supplies serving less than 5,000 people, and by the public water system governing board subject to the approval of the Commissioner of Health for supplies serving more than 5,000 people, as described in the Public Health Law (PHL).  Protection zones serve to prioritize the effort of the public water system when administrating this Section.  Rules and regulations become more stringent as the protection zones near the water supply intake.

2.	Watersheds and protection zone maps shall be drawn on United States Geological Survey (USGS) topographical maps in order to minimize confusion and clearly delineate protection zone boundaries.  The City of Ithaca shall confirm that protection zones boundaries are consistent with those of the watershed boundary.

3.	Inspections of the watershed may be made, in accordance with the authority provided under Section 1101 of the PHL, by the City of Ithaca in accordance with a schedule developed by the City of Ithaca Department of Public Works, subject to review by the Tompkins County Health Department.

4.	Permits and approvals by state agencies or political subdivisions, as they relate to water supply source protection, will be monitored by the public water system.  The public water system may monitor permits and approvals for the manufacture, use, storage, and disposal of any products, materials or by-products, such as wastes within the protection zones that will adversely affect the sources of water supply.  These permits may include, but are not limited to, SPDES permit; onsite disposal systems; land application of waste; disposal wells; recharge basins; landfills; septage and sludge disposal; hazardous materials manufacturing, storage, transportation, use and disposal; radiological material; waste lagoons and pits; pesticide storage and use – probably want to add SWIPs.  The City of Ithaca’s purpose for monitoring these permits is to assure compliance with the requirement of this Section.

a.)	Environmental assessment actions and permits issued for a regulated activity by a local, county, state and/or federal agency that requires a public hearing will be the vehicle by which the City of Ithaca will become informed of the proposed action or issuance.  This hearing process will provide the forum for the City of Ithaca to ensure compliance with this Section.

b.)	Environmental assessment actions and permits issued for a regulated activity by a local, county, state and/or federal agency that do not require a public hearing, may not provide the public water system with an opportunity to become informed of and ensure compliance with this Section.

c.)	The City of Ithaca may implement a procedure to monitor other permitted actions issued by a local, county, state and/or federal agency that do not require an environmental assessment action.

5.	Monitoring of water quality in the protection zones shall be the responsibility of the City of Ithaca and the New York State Department of Health – just a note, the HD does annual monitoring only related to the infrastructure – they will be not be looking upstream..  A monitoring schedule, developed by the City of Ithaca, shall be subject to review and approval by the Tompkins County Health Department.  Results from this monitoring are expected to provide the basis for determining changes in water quality of the water supply, over time.  This requirement is in addition to any intake raw water monitoring.

6.	SPDES permitted properties, facilities and activities.  SPDES or the State Pollution Discharge Elimination System includes the issuance of permits that authorize discharges to waters of the state by specific properties, facilities, and/or activities.  Discharges in compliance with a current SPDES permit shall be deemed in compliance with this Section.

7.	An inventory, census and summary report shall be initiated and updated on a regular basis by the City of Ithaca, of all properties, facilities, and activities in the protection zones that may contribute to water supply source contamination.  This inventory, census and summary report may include, but is not limited to, changes in and trends of the following:

a.)	land, property, and facility use;

b.)	population;

c.)	onsite disposal system;

d.)	dwelling units;

e.)	domestic animals (livestock and fowl);

f.)	pesticide and herbicide storage and use;

g.)	deicing salt storage and application;

h.)	landfills and refuse disposal areas;

i.)	waste storage pits and lagoons;

j.)	animal waste storage;

k.)	land application of waste, sludge and septage disposal;

1.)	disposal wells;

m.)	recharge basins;

n.)	toxic waste production, storage, transportation and use;

o.)	fertilizer storage and application;

p.)	surface and underground storage of gasoline, oil or other contaminating materials;

q.)	commercial and industrial activity;

r.)	point source discharges;

s.)	storm sewer discharges;

t.)	junkyards;

u.)	compost facilities;

v.)	accidental spills;

w.) sediment generation and control practices; and

x.)  permits issued to regulate systems, facilities and activities.

8.	Variances to this Section may be granted by the Commissioner of Health after considering and making a finding on each of the following six factors:

I.)	Whether the property, facility and/or activity to be authorized by the variance is compatible with the purpose of this Section.

II.)	Whether the health and safety of the water consuming public will be protected as a result of the treatment provided or other remedial action taken.

III.)	Whether any hardship can be alleviated by some other method that is feasible for the applicant to pursue.

IV.)	After considering all existing local conditions, including allowed uses, whether the property, facility and/or activity, in question, cannot yield an equivalent benefit to the applicant if used for any other type purpose that would comply with this Section.

V.)	Whether the variance requested is the minimum variance necessary to provide relief from any hardship or additional latitude provided due to a specific circumstance.

VI.)	Whether any hardship was created by this Section or the applicant or the applicant’s successor.

Such variances shall be given in writing and only given after a public hearing on the question has been held in Tompkins County.  Should such variance to this Section cause a significant threat to the life, health, or safety of the water consuming public, the Commissioner may order that such variance, in whole or in part, either conform to the requirements of this Section within a limited period of time, at the Commissioner's discretion, or be discontinued immediately.  The issuance of a variance from this Section shall not act as a variance from any other regulation or requirement, or permit any use or extension of use requiring action, of any other local, state or federal agency.

All non-conforming properties, facilities, and/or activities, not provided with a variance shall be subject to this Section on its effective date and expected to be in compliance within one year of this Section’s effective date.  A “compliance schedule” beyond this one year deadline, may be approved by the City of Ithaca Board of Public Works subject to change by the Commissioner of Health.

The Commissioner of Health may request that the City of Ithaca review any request for a variance prior to making a determination on the request.  The Commissioner may impose such variance approval conditions as deemed necessary to serve the purpose and intent of this Section.  Non-compliance with these variance approval conditions shall be deemed a violation of this Section.

In the event that any non-conforming property, facility and/or activity is vacated and/or discontinued for a period equal to or greater than six continuous months, any variance from this Section may be nullified by the Commissioner of Health.

a.)	Pre-approved Variances.  Prior to submission of the final public water system version of this Section, the following list of properties, facilities and/or activities has been granted a variance, from this Section, for the specific non-complying property, facility and/or activity stated:

1.)

2.)Might be necessary to get buy in from upstream towns.  Could be clear that changes to use/ownership will result in loss of variance.  Or will require review and compliance with measure, or something like that.

3.)

et cetera

These variances have been granted as a result of the public water system's determination that compliance of the property, facility and/or activity will cause undue hardship and that the property, facility, and/or activity alone or cumulatively with others will not cause the contamination or the degradation to the source of water supply that this Section is intended to protect.  Such variances may be conditioned upon the implementation of required mitigation measures to ensure water supply source protection.  Any change in the property, facility and/or activity or failure to complete any mitigation measures may cause such a variance to be revoked by and at the discretion of the Commissioner of Health.

New or more strict regulations adopted after the effective date of this Section may cause a variance listed above to be reconsidered by the Commissioner of Health.

b.)	Variances Following Promulgation of this Section.  Applicants requesting a variance from this Section, subsequent to the submission of the final City of Ithaca version of this Section, shall submit a registered letter to the City of Ithaca Board of Public Works containing at least, but not limited to, responses to the following minimum required information:

i.)	The applicant’s name, address, telephone number(s) and interest in the subject property, facility, and/or activity and the owner’s name, address and telephone number(s), if different from the applicant, and the owner’s signed consent to file the application.

ii.)	The protection zone location, along with the street address and either a copy of the recorded plat or legal description of the property, facility and/or activity.

iii.)	A narrative description of the non-conforming nature of the property, facility and/or activity together with any pertinent information that may be necessary to adequately review the application.

iv.)	A site plan illustrating the location of the non-conforming issue and site conditions, such as reasonably detailed contours and drainage patterns.

v.)	A detailed statement describing the hardship imposed by the enforcement and administration of this Section, specifically addressing the basis of the six variance factors referred to at the beginning of E.8. of this Section and the minimum variance necessary to provide relief.

vi.)	A statement from a New York State licensed professional trained in surface and ground water quality assessing the potential impact of authorization of the requested variance on the surface or ground water supply, and in particular how such potential impact on the source of water supply this Section intends to protect will be mitigated.  Where are they supposed to find this person?

vii.)	A statement from the applicant and owner agreeing to:

A.)	Comply with all conditions of a variance authorization

B.)	Submit a written annual report to the public water system governing board for approval that shall include but not be limited to the following information:

1.	Any changes in the property, facility and/or activity since either the variance was authorized or the previous annual report submittal.

2.	A summary and copy of any monitoring or testing results received by the applicant and/or owner relating to water quality.

3.	A report on any incidence of non-compliance with any conditions of the variance or other part of this Section and what action(s) taken in order to return to compliance.

C.)	Develop, receive approval of, and implement a plan to protect the surface and ground water supply source from potential contamination associated with the property, facility and/or activity.  This plan shall include but not be limited to the following:

1.	A description of operating procedures implemented in order to meet the conditions of the authorized variance that incorporate applicable best management practices.

2.	A drainage control plan implemented in order to meet the conditions of the authorized variance.

3.	A property, facility and/or activity specific waste disposal program and procedure guide.

If, in the opinion of the Commissioner of Health, compliance with all conditions of the authorized variance fail to meet the purpose of this Section, the applicant and/or owner shall immediately terminate the offending use or activity and shall remediate any contamination of the surface or ground water supply source.

9.	Appeals of this Section shall be undertaken as follows:

a.)	An appeal of a denial of an application for approval of a regulated activity, or of an application for approval of a variance, or of an alteration or modification of a regulated activity or noncomplying regulated activity shall be in such a manner as is provided by law.

b.)	An appeal of a modification, suspension or revocation of an approval of a regulated activity or of any variance issued by the Commissioner of Health shall be in such a  manner as is provided by law.

10.	Enforcement of this Section shall be undertaken pursuant to PHL Section 1102 and 1103, and may ultimately result in an application of the Commissioner of Health to any court of competent jurisdiction. Enforcement shall be initiated by the City of Ithaca delivering formal notice to the property owner of the City of Ithaca’s determination of any apparent or actual violation of this Section. Such notice shall include a copy of the rule or regulation of this Section that has been apparently or actually violated and the action necessary to reach compliance. If such notice does not result in compliance within a reasonable period after the original notice date, as determined by the City of Ithaca, the Tompkins County Health Department (TCHD) shall be informed and assume further enforcement responsibility. If the activity does not result in compliance within a reasonable period following the TCHD initial action, as determined by the TCHD, the Commissioner of Health shall be informed and assume ultimate enforcement responsibility. What can they do?  Is there any real enforcement option?

a.)	Prior to the PHL enforcement proceedings described above, the public water system will attempt to resolve any non-compliance with this Section through more informal channels.  Apparent non-compliance within the agricultural and farm industry will be coordinated with representatives of the Tompkins County Soil and Water Conservation District (TCSWCD).  The TCSWCD may assist with other apparent non-complying activities as well.

b.)	The City of Ithaca will provide the owner of the apparent non-complying activity with the information necessary to understand the nature of the non-compliance.  The owner may rely on the support of representatives from the public or private agency of their choice to assist in the response to the City of Ithaca’s informal and any formal proceedings.

c.)	Issues related to properties, facilities, and/or activities that border two or more watersheds (and therefore possibly subject to two or more sets of watershed rules and regulations), will be explained to the property owner by the City of Ithaca prior to any formal enforcement proceedings.

d.)	Once the formal enforcement proceedings begin, the Tompkins County Board of Health may at any time intercede and attempt to resolve the non-compliance or related issue.

11.	Separability and Validity.  If any provision of this Section is held invalid, such invalidity shall not affect other provisions, which shall be given effect without the invalid provisions.

12.	Amendments.  Except as noted in the Variance part of this Section, amendments to these rules and regulations are considered revisions and therefore required the City of Ithaca to follow the same adoption procedures required for the originally established rules and regulations.

F.	Ground Water:

1.	Protection Zones for Ground Water Sources.  Zone I-G is the well-head protection area.  Zone II-G is the recharge area(s) for ground water or aquifers. Zone III-G is the watershed area tributary to the recharge area(s) as defined earlier.  The specific rules and regulations that follow become more stringent as one moves from Zone III-G to Zone I-G. Zone I-G is included in Zone II-G and III-G; and Zone II-G is included in Zone III-G. An illustration of these zones is shown on Appendix D.Need a visual

2.	Specific Regulations, Zone III-G (Watershed tributary to the recharge area Zone II-G):

a.)	Onsite Disposal Systems:

1.)	A permit from the Tompkins County Health Department is required prior to the installation of any individual, or nonmunicipal sewage disposal system in Tompkins County.  Outside of Tompkins County, this permit must be obtained from the county Health Department, from the district health office, the New York State Department of Environmental Conservation or municipality having jurisdiction.

2.)	The design, construction and operation of the sewage system shall conform to the applicable standards and permit requirements of the permit-issuing office.  Generally, these are based on and are at least as strict as (a) the standards contained in 10 NYCRR 75 for systems with flows of 1,000 gallons per day or less of sanitary wastes that discharge to the ground water, and (b) the New York State Department of Environmental Conservation standards for systems with flows in excess of 1,000 gallons per day or those that contain industrial waste or that discharge to a surface water.

3.)	No ground water discharging portion of a sewage system shall be constructed, placed, or rebuilt within 100 linear feet distance of any lake, reservoir or their tributary streams unless a specific waiver has been issued by the permit-issuing office.

b.)	Point Source Discharge:  Point-source discharges, including those from boats, are prohibited except as allowed per state and federal rules and regulations.

c.)	Storm Sewer Outlets: Storm sewer outlets shall be designed and installed in accordance with the best management practices (BMP) defined earlier in this Section and local, state, and/or federal rules and regulations.

d.)	Snow Disposal:  Routine dumping of snow removed from streets, roads and parking areas directly into Zone II-G or streams flowing into Zone II-G is prohibited where such routine dumping violates local state, and/or federal law.

e.)	Refuse Disposal Areas and Junkyards:

1.)	Refuse disposal areas shall not be located on or beneath the surface of the ground within a 250 feet linear distance of Zone II-G or any watercourse flowing into Zone II-G.

2.)	Solid waste disposal facilities shall conform to 6 NYCRR 360; shall have been issued the required construction and operating permit; and shall operate in accordance with such permits.

3.)	Abandoned refuse disposal areas, sites, landfills and dumps will be identified by the public water system, and reported to the New York State Department of Environmental Conservation for investigation.  The public water system shall track any investigations and/or remedial actions.

4.)	No junkyards shall be located within a 250 feet linear distance of Zone II-G or any watercourse flowing into Zone II-G.

f.)	Animal Wastes Storage and Disposal:  Areas used for the storage, stockpiling, or disposal of non-agricultural or agricultural associated animal waste shall be in conformance with the standard BMP defined earlier in this Section.

g.)	Sewage, Septage and Sludge:  Disposal and/or storage of sewage, septage and municipal sludge is prohibited where such disposal and/or storage violates local, state, and/or federal law.

h.)	Hazardous Substances:

1.)	Storage, disposal, and/or transportation of hazardous substances is prohibited where such storage, disposal, and/or transportation violates local, state, and/or federal law.

2.)	Hazardous substances and petroleum products shall not be allowed to enter surface or ground waters.

i.)	Radioactive Material:  Disposal of radioactive material is prohibited where such disposal violates local, state, and/or federal law.

j.)	Fertilizer Use:

1.)	Storage and use of fertilizers for agricultural purposes shall be in conformance with the standard best management practices (BMP) defined earlier in this Section.

2.)	Fertilizer use for non-agricultural and non-residential application shall be in accordance with BMP acceptable to the TCSWCD.

k.)	Pesticide Use:  The storage, application, use, discharge, and/or disposal of pesticides:

1.)	Is prohibited where such storage, application, use, discharge, and/or disposal of violates State of Federal law.

2.)	Shall be in conformance with the standard best management practices (BMP) defined earlier in this Section.

3.)	For non-agricultural and non-residential purposes shall be in accordance with BMP acceptable to the TCSWCD.

l.)	Releases, Discharges, and Spills:

1.)	Pursuant to Navigation Law, Article 12, Sections 170 through 197, discharges of petroleum shall be reported to the NYSDEC Spill Response Hotline (800) 457-7362 immediately, but in no case later than two hours after a discharge, and must be cleaned up.

2.)	Pursuant to Section 311(b)(3) of the Clean Water Act, immediate notification of the federal National Response Center (800) 424-8802 is required as soon as there is knowledge of an oil discharge that violates water quality standards or causes sheen on navigable waters.

3.)	Any release of a hazardous substance in an amount greater than a reportable quantity must be reported to the NYSDEC under 6 NYCRR Parts 595, 596, 597 and to the federal National Response Center (800) 424-8802 under the federal Water Pollution Control Act and 40 CFR Part 117.21.

4.)	Underground storage of petroleum products or any other contaminating material is prohibited except as permitted by applicable state and federal rules and regulations.

m.)	Stockpiles:

1.)	Storage of chloride salts is prohibited within a 500 feet linear distance of Zone II-G or any stream flowing into Zone II-G where such storage violates local, state, and/or federal law.

2.)	Storage of coal or of coal by-products  is prohibited where such storage violates local, state, and/or federal law.

3.)	Compost facilities shall be managed in accordance with 6 NYCCR, Part 360.

n.)	Deicing Substances Application:  Use of deicing substances by commercial, industrial or governmental entities shall be restricted to the amounts necessary to protect public safety as set forth in the "New York State Department of Transportation Guidelines for Snow and Ice Control Materials 1989-90 Winter Season and Beyond." A copy of this guide or its successor shall be acquired and kept on file by the public water system.

o.)	Cemeteries:  No burial of a human or animal body shall be made within 250 feet linear distance of Zone II-G or any streams flowing into Zone II-G.

p.)	Sediment Generation:

1.)	Farm tillage practices shall be in conformance with the standard best management practices (BMP) defined earlier in this Section.

2.)	All land-distributing activity including, but not limited to, general construction, highway construction, access road construction and road maintenance shall be in conformance with the standard best management practices (BMP) defined earlier in this Section.

3.)	Pursuant to the federal Water Quality Act of 1987 (Clean Water Act Amendments), construction activities, including clearing, grading and excavation activities, if the disturbed area is more than five acres, or less than five acres if it is part of a larger plan of development or sale, are classified as associated with industrial activity and must therefore fulfill federal and state storm water permitting requirements prior to discharging storm water from the site.

3.)	Specific Regulations, Zone II-G (Recharge Area for Ground Water or Aquifers-- for the purposes herein it is assumed that an aquifer could be confined or unconfined, consolidated or bedrock.  The boundary of Zone II-G will be "well specific"):

a.)	Land Application of Waste:  Land application of waste is prohibited.

b.)	Untreated Discharges:  Untreated discharges of any kind shall be minimized using standard BMP defined earlier in this Section.

c.)	Storm Water Runoff Recharge Basins:  Use of storm water recharge basins shall be minimized using standard BMP defined earlier in this Section .

d.)	Snow Disposal:  The routine stockpiling of snow removed from roadways and parking areas on the ground surface shall be minimized using standard BMP defined earlier in this Section.

e.)	Refuse Disposal Areas and Junkyards:

l.)	The establishment of refuse disposal areas and junkyards is prohibited.  The continued operation of existing refuse disposal areas is prohibited after three years of the adoption of these rules and regulations.

2.)	A comprehensive monitoring program for existing and abandoned refuse disposal areas in accordance with 6 NYCRR 360 is required.

f.)	Animal Wastes:  Animal wastes, including but not limited to, manure piles, feedlots, barnyards, and yarding areas, shall not be concentrated, except where provisions have been made to prevent seepage into ground water.

g.)	Land Application of Septage and Municipal Sludges:  Land application of septage and municipal sludges shall be minimized using standard BMP defined earlier in this Section.

h.)	Leaking Sewers:

1.)	All sewers installed shall be as tight as the state of the art allows.

2.)	Remedial measures shall be taken by the owner if evidence indicates excessive infiltration or exfiltration is occurring.

3.)	New sewers shall meet the tightness specifications for water mains as a minimum.

i.)	Waste Lagoons and Pits:  Use of lagoons and pits for temporary storage of waste shall be minimized using standard BMP defined earlier in this Section.  All storage facilities shall be designed to prevent infiltration into ground water and, when required, under permit by the Department of Environmental Conservation.

j.)	Radioactive Material:  Transportation of radioactive material is prohibited except under permit of the Department of Transportation.

k.)	Stockpiles:  Storage of chloride salts is prohibited except in waterproof buildings or in water-tight vessels.

l.)	Underground Storage Tanks and Pipelines:  Underground storage of petroleum products or any hazardous substances or radioactive material is prohibited except as permitted by the Department of Environmental Conservation.

m.)	Improperly Constructed or Abandoned Wells:

1.)	All oil and gas wells shall be constructed in accordance with the requirements of the Department of Environmental Conservation.

2.)	All water supply wells shall be constructed in accordance with the requirements of the Department of Health.

3.)	All abandoned wells shall be sealed in accordance with state and federal requirements for oil and gas wells and requirements for water supply wells.

o.)	Salt Water Intrusion:  Any water supply wells or any other water wells which allow salt water intrusion shall be taken out of service and properly abandoned.

4.	Specific Regulations, Zone I-G (Well-Head Protection Area -- for the purposes herein the well-head protection area assumes that an aquifer could be confined or unconfined, consolidated or bedrock.  The boundary of Zone I-G will be "well specific"):

a.)	All land shall be protected and controlled through direct ownership of the land or through the acquisition of protective easements or other appropriate measures by the public water system in order to prevent pollution of the ground or ground water.

b.)	All systems, facilities and activities that may create any untreated discharge are prohibited except for the physical water supply pumping and treatment facilities and controls.

c.)	All well-heads and containment buildings must be in conformance with federal, state and local flood plain management or similar regulations or ordinances to prevent their contamination by flood waters.  This area shall further be protected from pollution by surface waters originating outside thereof by the construction of suitable diversion ditches or embankments.

d.)	The water supply pumping facilities and controls shall be protected against damage from tampering by fencing or other suitable enclosures or by their manner of construction and installation.  The area shall be posted prohibiting trespass for any purpose.

G. Surface Water:

1.	Protection Zones for Surface Water Sources.  Zone I-S includes surface water area within 1,000 feet of an intake.  Zone II-S includes surface water area within one mile of an intake.  Zone III-S includes surface water and land area from all or part of the tributary watershed. Zone IV-S includes remaining water and land area within a watershed not included in Zone III-S.  Detailed definitions of protection zones by categories are found earlier in this Section.  The specific rules and regulations that follow become more stringent as one moves from Zone IV-S to Zone I-S. Zone I-S is included in Zones II, III and IV-S. Zone II-S is included in Zone III and IV-S.  Zone III-S is included in Zone IV-S.  Appendix A, B and C show typical surface water protection zones.

2.	Categories of Surface Water Supply Sources.  The categories of surface water supply sources shall be lakes, reservoirs and watercourses.

3.	Specific Regulations, Zone IV-S (remaining land and water area of watershed outside of Zone III-S):

a.)	Protection Zone Knowledge -- public water system shall maintain information on any property, facility, and/or activity within this zone that could pose a pollution threat to the source of water supply of the public water system.

b.)	Compliance -- violations of any general water pollution control program and related federal or state environmental protection rules and regulations shall require enforcement action in accordance with these rules and regulations.

4.	Specific Regulations, Zone III-S (water and land area from all or part of tributary watershed):

a.)	Onsite Disposal Systems:

1.)	A permit from the Tompkins County Health Department is required prior to the installation of any individual, or non-municipal sewage disposal system in Tompkins County.  Outside of Tompkins County, this permit must be obtained from the county Health Department, from the district health office, the New York State Department of Environmental Conservation or municipality having jurisdiction.

2.)	The design, construction and operation of the sewage system shall conform to the applicable standards and permit requirements of the permit-issuing office.  Generally, these are based on and are at least as strict as (a) the standards contained in 10 NYCRR 75 for systems with flows of 1,000 gallons per day or less of sanitary waste that discharge to the ground water, and (b) the New York State Department of Environmental Conservation standards for systems with flows in excess of 1,000 gallons per day or those that contain industrial waste or that discharge to a surface water.

3.)	No ground water discharging portion of a sewage system shall be constructed, placed or rebuilt within 100 feet limiting distance of any lake, reservoir or their tributary watercourses unless a specific waiver has been issued by the permit-issuing office.

b.)	Point Source Discharges:  Point source discharges, including those from boats, are prohibited, except as allowed in accordance with state and federal rules and regulations.

c.)	Storm Water Outlets:  Storm water outlets shall be designed and installed in accordance with the standard BMP defined earlier in this Section.  Such outlets shall not be made directly to any lake, reservoir, or their tributary watercourses that would violate local, state, and/or federal law.

d.)	Snow Disposal:  Routine dumping of snow removed from streets, roads and parking areas directly into any lake, reservoir, or their tributary watercourses is prohibited.

e.)	Refuse Disposal Areas and Junkyards:

1.)	No refuse disposal area shall be located within a 250 feet linear distance off any lake, reservoir or their tributary watercourses.

2.)	Solid waste disposal facilities shall conform to 6 NYCRR 360; shall have been issued the required construction and operating permits; and shall operate in accordance with such permits.

3.)	Abandoned refuse disposal sites, landfills and dumps will be identified by the public water system, and reported to the New York State Department of Environmental Conservation for investigation.  The public water system shall track any investigations and/or remedial actions.

4.)	No junkyard shall be located within a 250 feet linear distance of any lake, reservoir, or their tributary watercourses.

f.)	Animal Wastes Storage and Disposal:  Areas used for the storage, stockpiling, or disposal of non-agricultural or agricultural associated animal waste shall be in conformance with the standard BMP defined earlier in this Section.

g.)	Sewage, Septage and Sludge: Disposal and/or storage of sewage, septage, and municipal sludge is prohibited where such disposal and/or storage violates local, state, and/or federal law.

h.)	Hazardous Substances:

1.)	Storage, disposal, and/or transportation of hazardous substances is prohibited where such storage, disposal, and/or transportation violates local, state, and/or federal law.

2.)	Hazardous substances and petroleum products shall not be buried in the soil, spread upon the surface of the ground or allowed to enter surface waters.

i.)	Radioactive Material: Disposal of radioactive material is prohibited where such disposal violates local, state, and/or federal law.

j.)	Fertilizer Use:

1.)	Storage and use of fertilizers for agricultural purposes shall be in conformance with the standard BMP defined earlier in this Section.

2.)	Fertilizer use for non-agricultural and non-residential application shall be in accordance with BMP acceptable to the TCSWCD.

k.)	Pesticide Use:  The storage, application, use, discharge, and/or disposal of pesticides:

1.)	Is prohibited where such storage, application, use, discharge, and/or disposal of violates State of Federal law.

2.)	Shall be in conformance with the standard best management practices (BMP) defined earlier in this Section.

3.)	For non-agricultural and non-residential purposes shall be in accordance with BMP acceptable to the TCSWCD.

1.)	Releases, Discharges and Spills:

1.)	Pursuant to Navigation Law, Article 12, Sections 170 through 197, discharges of petroleum shall be reported to the NYS DEC Spill Response Hotline (800) 457-7362 immediately, but in no case later than two hours after a discharge, and must be cleaned up.

2.)	Pursuant to Section 31 l(b)(3) of the Clean Water Act, immediate notification of the federal National Response Center (800) 424-8802 is required as soon as there is knowledge of an oil discharge that violates water quality standards or causes sheen on navigable waters.

3.)	Any release of a hazardous substance in an amount greater than a reportable quantity must be reported to the NYS DEC under 6 NYCRR Parts 595, 596, 597 and to the federal National Response Center (800) 424-8802 under the federal Water Pollution Control Act and 40 CFR Part 117.21.

4.)	Spills of any other material stored in bulk shall be reported as required by ECL Section 17-1743. Clean-up of spills is the responsibility of the owner. In cases of material in transit, clean-up is the responsibility of the carrier.

5.)	Any person that recognizes or suspects a release, discharge or spill shall notify the public water system and the Tompkins County Office of Environmental Health of all releases, discharges or spills identified above

m.)	Stockpiles:

1.)	Storage of chloride salts is prohibited within a 500 feet linear distance of any lake, reservoir, or their tributary watercourses where such storage violates local, state, and/or federal law.

2.)	Storage of coal or coal by-products is prohibited where such storage violates local, state, and/or local law.

3.)	Compost Facilities shall be managed in accordance with 6 NYCRR, Part 360.

n.)	Deicing Salt Application: Use of deicing substances by commercial, industrial or governmental entities shall be restricted to the amounts necessary to protect public safety as set forth in the "New York State Department of Transportation Guidelines for Snow and Ice Control Materials 1989-90 Winter Season and Beyond."  A copy of the guide or its successor shall be acquired and kept on file by the public water system.

o.)	Cemeteries: No burial of a human or animal body shall be made within a 250 feet linear distance of any lake, reservoir, or their tributary watercourses.

p.)	Sediment Generation:

1.)	Farm tillage practices shall be in conformance with the standard BMP defined earlier in this Section.

2.)	All land-disturbing activity, including, but not limited to, general construction, highway construction, access road construction, and road maintenance shall be in conformance with the standard BMP defined earlier in this Section.

3.)	Pursuant to the federal Water Quality Act of 1987 (Clean Water Act Amendments), construction activities, including, clearing, grading and excavation activities, if the disturbed area is more than five acres, or less than five acres if it is part of a larger plan of development or sale, are classified as associated with industrial activity and must therefore fulfill federal and state storm water permitting requirements prior to discharging storm water from the site.

q.)	Recreation:  Recreational land and water use shall be managed to prevent any adverse impact on water quality.

r.)	Impoundment Releases:  Releases from impoundments shall be managed so as to prevent adverse environmental downstream impacts on water quality.

5.	Specific Regulations, Zone II-S (includes water surface area one mile upstream of intake):

a.)	Point Source Discharges:  The point source discharge of waste is prohibited.  This shall include, but not be limited to, that:

1.)	for which a State Pollution Discharge Elimination System permit is required;

2.)	from storm water, diversion ditches, culverts and all other sources: and

3.)	from commercial and recreational boats.

b.)	Recreation Use:  In reservoirs, recreation is prohibited except for permitted fishing from shoreline or by using a non-motorized boat.

c.)	Foreign Matter:  No waste or other matter shall be discharged, placed, applied or thrown into these waters including herbicides or pesticides except for the application of copper sulfate for control of algae with the approval of the NYSDEC and knowledge and permission of the public water system.

6.	Specific Regulations Zone I-S (includes surface water area within 1000 feet of intake):

a.)	Water and Land Use:

1.)	Water If left this way it would mean that – but these are not in effect for any water system.  Bolton Point would have to address it in some other way – the volume of water to pollutant ratio is skewed heavily in the favor of not worrying too much about it.  surface use including recreational activities is prohibited.  Notification of the public of these restrictions shall be made by posting signs in appropriate locations.  The public water system shall perform regular patrols during recreation season(s) to enforce this restriction.

2.)	A strip of land 600 feet in width and 1000 feet in length shall be reserved, surrounding a lake water supply intake, where no intensive land use including recreational activities is allowed.  This land shall be controlled to prevent pollution of the ground or surface water by direct ownership of the land or by the acquisition of protective easements or other appropriate measures.

3.)	A strip of land 300 feet in width and 500 feet in length shall be reserved around reservoir water supply intakes where no intensive land use including recreational activities shall be allowed.  The land shall be controlled to prevent pollution of the ground or surface water by direct ownership of the land or by the acquisition of protective easements or other appropriate measures.

b.)	Foreign Matter:  No waste or other matter shall be discharged, placed, applied or thrown into these waters including herbicides or pesticides.

# Comments

This is the language from our old regs, but broader to encompass zone 1 & 2. Need Roxy’s help w/ this.

Do we have more up to date publications to rely upon

Does this Whole Farm Planning Program exist?

City Code does not have # of vehicles that make it a junkyard, Tompkins County may have 20 car limit, but could not find it in County Code.

Take out reference here, but could leave in and say its BPW or Common Council, but that may be larger policy decision that doesn't need to be part of DOH regs.

Is this something we want to do?

Need map

Can we comply with this now?

anything more recent than this?

could this apply to fracking waste or pumped out waste? should this be stricter over minimized?

strictrer for HVHF?

include something specific to HVHF construction by DEC regs

doesn't seem to be anything to prohibit fracking in  these zones. anything we can put in here?

update source?

prohibits water surface use - does this mean no recreational activity on Cayuga Lake?